Automatic Watering system

If the system has to be reset, follow these steps.

Press reset.

Select language by:  turning dial to language; press rain delay button one;  press next until you reach English; press enter to confirm; press rain delay again or turn rotary dial to exit this mode.

Set date/time by: turn rotary dial to date and time position; press and hold + to advance clock to correct time; press enter to save correct time; repeat process to set year, month and date.

Program watering for cycles A, B and C as follows:

Set dial to cycle start times for A: set start time as 11.30pm using + and – buttons, then press enter.

Set dial to watering days for A: press next to cycle through the possibilities.   In order for the system to water every day when program A is selected you need to select each day of the week.  Press next until a day of the week flashes, press enter to select that day and continue until every day of the week has been selected and displays a raindrop.

Slide the duration slider for channels 9, 10 and 12 to 15 minutes.  (Leave the others at off.)

Slide the program selector slider to A for channels 9, 10 and 12.

Set dial to cycle start times for B: set start time as 11.30pm using + and – buttons, then press enter.

Set dial to watering days for B: press next to cycle through the possibilities.   In order for the system to water every other day when program B is selected you need to press next until odd flashes on the display and then press enter.

Set dial to cycle start times for C: set start time as 11.30pm using + and – buttons, then press enter.

Set dial to watering days for C: press next to cycle through the possibilities.   In order for the system to water at 4 day intervals when program C is selected you need to press next until interval flashes on the display, then select the interval as four by pressing the + and – buttons and then press enter.

During high summer when frequent watering is needed, program A should be selected but when less frequent watering is needed, channels 9, 10 and 12 should instead be set to B or C.

Rain sensor should be set to ON.